MPTCP
Multipath TCP
2023-05-23 uablrek@gmail.com

---
Multipath TCP
- Adds “multihoming” for TCP to allow redundancy and higher throughput
- Impact on client and server code is minimal (or none)
- For network infra structure it looks like multiple normal TCP connections
- Is prepared for NAT (as opposed to multihomed SCTP)
- Support in Linux (and iproute2) is fairly new. Used by Apple for some time (iPhone)
- In Telco it can perhaps become a modern alternative to SCTP? (Diameter can be carried on TCP, why not MPTCP)
- Support in go is planned to v1.21 (August 2023)

---
Network topology

---
Demo
- Start cluster. Show (destination-) routing on paths (ping)
- Setup endpoints and traffic with mptcp.c. Check sockets. Tcpdump on routers, and block the upper path (failover)
- Use “mptcpize” (LD_PRELOAD) to enforce mptcp on a mptcp-unaware program. (show the “nc” pitfall)
- Use a systemtap program to enforce mptcp on ctraffic (LD_PRELOAD can’t be used for statically linked (go) programs)

---
References
- Wikipedia Multipath TCP
- rfc8684
- Support in go v1.21
- How to setup and configure mptcp on Ubuntu
- Xcluster ovl/mptcp (this demo)